## Slide 1: Ch. 4. Measurements (on Site) in Field
pH와 EH
  Basic water quality parameters
  Definitions
    pH = -log10aH+ (logarithmic value of the reciprocal of the proton activity in the solution)
    EH: Electrode potential against hydrogen reference electrode. Indicating the electrode concentration in a solution
  Both measures electrode potential with probes
  Preliminary knowledge on a electrochemical cell required
    oxidation state: charges on an ion, assuming a perfect ionic bonding
    oxidation-reduction: Increase-decrease of oxidation state
    cathode-anode: electrode where reduction-oxidation occur

## Slide 2: Ch. 4.
Typical electrochemical cell
http://chem-guide.blogspot.kr/2010/04/electrochemical-cell.html

## Slide 3: Ch. 4.
Principles
  For the following general redox reaction
    aA + bB =cC + dD + ne-
  Nernst equation
    (G=-nFE)
    EH: electrode potential
    Eo; standard electrode potential
    R; ideal gas constant, 0.001987 kcal/K
    T; absolute temperature
    n; number of electrons transferred
    F: Faraday constant, 23.06 kcal/V.mole

## Slide 4: Ch. 4.
Hydrogen electrode
http://chemwiki.ucdavis.edu/Analytical_Chemistry/Analytical_Chemistry_2.0/11_Electrochemical_Methods/11B_Potentiometric_Methods

## Slide 5: Ch. 4.
  Reaction on the hydrogen electrode
    0.5H2(g) = H+ + e-
    If atm., m, V
    If m
     pH is also a function of EH

## Slide 6: Ch. 4.
For the following half reaction in sample solution
  Fe2+ = Fe3+ + e-
The electrode potential measurement with hydrogen electrode as a reference electrode is for the following reaction
  0.5H2(g)+Fe3+ = H+ + Fe2+
  The electrode potential is given by
  * In most cases, hydrogen electrode is not actually used in real measurements

## Slide 7: Ch. 4.
Methods of measurement
  Colorimetric method: Measuring pH and EH from color change of the solution having and indicator  used no more.
  Electrometric method commonly used nowadays
    Potentiometer:
    Reference electrode: electrode used as a reference when the potential is measured
      Calomel elctrode (HgCl2-Hg)
      AgCl-Ag electrode
    Indicator electrode
      pH: glass electrode
      EH: platinum electrode
    Temperature compensator
      Automatic (ATC)
      Manual

## Slide 8: Ch. 4.
Notables at pH measurement
  Stablized only in a well buffered solution
  Difficult to obtain accurate values when T is lower than 25oC, concentrations of HCO3- is below 50mg/L, and pH is either lower than 4.5 or higher than 8.2
  The sample should be stationary during the measurement
  [Glass electrode]
    Note the asymmetric potential (Due to the difference between the inner and outer wall of the glass electrode, the potential become nonzero for the same concentrations)
    Calibration with buffere solutions
    Temperature compensation
    Measurement may become inaccurate, if the ionic strength of the sample solution is very different from that of the buffer solution
    Use a special elctrode when pH is lower than 1 or higher than 9
    Presoak in water for an hour before use
    The older the electrode, the slower and more inaccurate the response
    Careful not to scratch the surface of the electrode

## Slide 9: Ch. 4.
http://www.ti.com/ww/en/industrial/sensors/pH/learn.html
General structure of glass electrode.
(combination electrode)
* Protect the instrument from the direct sunlight

## Slide 10: Ch. 4.
Notables at EH measurement
  Meaningul only when DO is lower than 0.01ppm (Most surface waters have higher DO concentrations than this, and DO measurement instead is advised in this case)
  Most redox reactions in nature are irreversible
  If there are a lot of active organic material, this will dominate in EH determination and makes the reading unstable
  Stable EH values are possible only in “well poised systems”
  Measured EH values in nature are the results from several redox reactions combined
  Redox reactions of C, N, and S in the samples with abundant Fe are so slow that they cannot affect significantly on EH values.
  [Platinum electrode]
    Platinum hydroxide can form on the surface of the electrode in an oxygen-rich environmen
    H2S, H2, CH4, organic matter, and Fe hydroxide can interfere the measurement
    Frequently check the validity with Zobell solution
    “Poisoning”: Remove with the mixture of pyrex glass power and glyceline
    The minimum measured value would be the closest to the true value
    Mind flowing & suspension effect

## Slide 11: Ch. 4.
Conductivity
  Ability of having electric current – function of ionic concentrations, mobilities, charges, and temperature
  Definition
    Conductance: G – reciprocal values of resistivity, proportional to the area and inversely proportional to the length
    G = 1/R = k(A/L)
    k = specific conductivity
    Always report the values at 25oC.
  Unit
    Old unit: mhos/cm
    Modern unit: S/m (Siemen)
    S/cm = mhos/cm

## Slide 12: Ch. 4.
Notables at measurement
  Calibrate with conductivity reference solutions
  Temperture compensation
  refer “platinum electrode” section in the previous slide